Fast motion of the surface molecules deduced from the sum-frequency vibrational spectra of the homolog series of alcohols

Jaeho Sung and Doseok Kim

Department of Physics and Interdisciplinary Program of Integrated Biotechnology

Sogang University, Seoul 121-742, Korea

Sum-frequency generation (SFG) vibrational spectroscopy was used to investigate the surface molecular structure of the homolog series of alcohol molecules at the alcohol-air interface. It was found that some of the SFG signal strengths from the terminal methyl group of short chain alcohols (like methanol and ethanol) cannot be explained by assuming fixed molecular orientation in time. Introduction of the molecular orientational motion having time scale similar to- or smaller than the dephasing time of the vibrational mode of the terminal methyl group (~0.7 picosecond) was able to explain the reduction of the SFG signal by motional averaging effect [1]. The timescale m the increased molecular size and bulk viscosity.

Introduction

The molecules in liquids are constantly moving very fast. This molecular motion has been studied using various techniques including Rayleigh scattering and molecular dynamic simulation [2-7]. For librational motion, it is well known that rapid motion induces the reduction(?) of inhomogeneous linewidth of a vibrational resonance [8]. Pump-probe experiments with femtosecond pulses found out the timescale of orientational motion of the molecule in water, methanol, and ethanol was a few picoseconds [2-7].

Most of the studies up to now (above) have been about the molecules in bulk liquid. As surface molecules are in a very difference environment from those of the bulk, it would be interesting to study the motion of the surface molecules as compared to the bulk molecules. Even with this motivation there has been hardly any report regarding the motion of the surface molecules. Proper experimental tool to probe the molecules at the liquid surface exclusively has been main challenge. Using the surface specificity of the second-order nonlinear optical process, orientational motion of dye molecules (malachite green) at air-water interface was studied by orientational hole-burning followed by surface second-harmonic generation [9]. Interestingly, the timescale of the motion was slower than that for the same dye molecule immersed in bulk water. As malachite green was quite large in size, the timescale of the motion was ~500 ps. For common and more relevant molecules such as water and alcohol, the motion is expected to be much faster. However the experimental difficulty hasn’t allowed the study of the surface motion of these molecules.

In this report, we investigated the surface of alcohols using surface sum-frequency generation (SFG) vibrational spectroscopy. For smaller molecules (methanol and ethanol), the sum-frequency signal of CH3 anti-symmetric stretch mode (r-) for certain polarization combinations was nearly zero, and it grew as the molecules become bigger. Analysis of the data indicated that the motional averaging effect must be considered in the SFG spectra of small molecules. The timescale of the molecular motion deduced from the detailed analysis of the SFG peak strength showed the small surface molecules move very fast while the motion becomes slower as the molecular size increases.

Experimental

The SFG experiment employed a home-built optical parametric generator/amplifier (OPG/OPA) system pumped with a picosecond Nd:YAG laser (Continuum PY61-10, 10-Hz repetition rate). The OPG/OPA based on a LiNbO3 crystal generated a tunable IR pulse from 2.5 to 4 m, and the second harmonic of Nd:YAG laser fundamental beam was used as the visible input beam. Typical input energies were 1 mJ/pulse and ~200 J/pulse, and incident angles were vis=49o and IR=60o for the visible and the tunable infrared beams, respectively. The pulsewidths of the input beams were about 30 ps.

Theoretical Background

In this section, we give a brief description about the effect of fast molecular motion on SFG spectra as discussed in ref. [1] for convenience of later discussion. Second-order nonlinear polarization P(2)(SF) induced at the surface by two input fields E1(vis) and E2(IR) can be expressed as

(1)

where,

(2)

In Eq.(2), , ,  and  are the amplitude, resonance frequency, surface density of molecules and line-width of the q-th molecular vibrational mode, respectively.  is a time-dependent direction cosine between the laboratory coordinates  and the molecular coordinates. We neglected the inhomogeneous broadening assuming that the visible input is far from resonance. Figure 2 is different from Fig. 1 in…

Reference

[1] X. Wei and Y. R. Shen, Phys. Rev. Lett. 86, 4799 (2001).

[2] S. Woutersen, U. Emmerichs, and H. Bakker, J. Chem. Phys. 107, 1483 (1997); Y. L. A. Rezus, D. Madsen, and H. Bakker, J. Chem. Phys. 121, 10599 (2004).

[3] R. A. MacPhail, H. L. Strauss, R. G. Snyder, and C. A. Ellinger, J. Phys. Chem. 88, 334 (1984).

[4] R. L. Sutherland, Handbook of Nonlinear Optics (Marcel Dekker, New York, 1996).

[13] Bella, S. D.; Lanza, G.; Fragala, I.; Yizehaik, S.; Ratner, M. A.; Marks, T. J. J. Am. Chem. Soc. 1997, 119, 3003.

[14] Kajzar, F.; Swalen, J. D. Organic Thin Films for Waveguiding Nonlinear Optics; Overseas Publishers Association: Amsterdam, 1996.

Table 1. The impurity contents and pH values in ionic liquids of [BMIM]PF6 and [BMIM]BF4.

|  | [BMIM]PF6 | [BMIM]BF4 |
| --- | --- | --- |
| Grade* | Ultrahigh | Lower | Ultrahigh | Lower |
| pH | 7.58 | 7.63 | 7.46 | 7.81 |
| Water content | 60ppm | <0.11% | 60ppm | 1200ppm |
| Chloride content | 6ppm | 50ppm | 6ppm | 70ppm |

* Grade as suggested by the company.

Figure captions

Figure 1. molecular coordinates of the methyl group.

Figure 2. SFG spectra of various alcohols with different polarization combinations: (a): SSP, (b): PPP, and (c): SPS.

Figure 3. Ratio values extracted from fitted results.:(a) A(CH3ss, PPP)/A(CH3ss, SSP) (b) A(CH3as, PPP)/A(CH3ss, SSP (c) A(CH3as, SPS)/A(CH3ss, SSP)

Figure 1.

# Comments

Times New Roman, bold, 14pt, center-aligned

Times New Roman, bold, 11pt, Harvard comma

Times New Roman, bold and italic, 11 pt

Abstract -

Times New Roman, 11pt, aligned on both sides, Linespacing: 1.5

Use pagebreak (do not use Enter) to start a new papge, as we do here to separate main text from the Abstract. Times New Roman, bold, 14pt

Times New Roman, 11pt, Linespacing: 1.5 
No indentation for the 1st line. 
Aligned on both sides

Note the format for the reference

- usually at the end of the sentence

- use square bracket

- hyphen for more than 2 references

- period immediately after closing the bracket.

Use only single space after the comma or period

Single empty line between the paragraphs

This is how to introduce the acronym first.

Single empty line before the beginning of the new section

Single empty line after the section heading

Use symbol for the Greek letters in the text

Space between the number and the unit

Use only Mathtype for the equation

Equation would be center-aligned.

Equation number at the end with usual parenthesis

Equation is the part of the sentence, so don’t forget comma or period if needed.

This is the way we use to refer to the equation

This is the way to refer to the Figures.

Pagebreak to start a Reference section.

Square bracket followed by a single space, Initial followed by last name. Use Harvard comma, bold for volume number. Period at the end of the reference

We can use the multiple references under one number using the semicolon. Note most of the Journals don’t allow using multiple references.

Avoid using et al., and write the full list of authors.

This is the format to refer to the book.

This is the reference format for the ACS journals.

Tables comes after the Reference with a new page. Each table requires one separate page. Table heading comes before the table, Times New Roman, 11pt.

Table caption: Times New Roman, 10pt

Start at a new page (with pagebreak, of course), Times New Roman, bold, 14pt

Single line between each figure caption

Each figure requires a separate new page.